## Slide 1
Smart Fan Speed Controller
01 / 12
Temperature + humidity
Fuzzy Logic and Genetic Programming PBL
L.D. College of Engineering, Ahmedabad
Chemical Engineering, Division A
Kirtan Siddhapura 240280105071
Mahesh Bhaliya 240280105005
Manav Chauhan 240280105008
Haresh Raval 240280105065
Notes: Welcome. Our group presents a smart fan speed controller for the Fuzzy Logic and Genetic Programming subject at L. D. College of Engineering, Ahmedabad. We are four Chemical Engineering students from Division A. This project is a software simulation.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 2
Problem
02 / 12
Manual speed adjustment depends on the user noticing changing conditions.
A temperature-only threshold ignores humidity and can switch abruptly.
Our model requests airflow from both inputs. It does not predict room cooling or moisture removal.
Notes: Manual fan adjustment requires attention as room conditions change. A simple temperature threshold ignores humidity. We use two inputs to create an interpretable fan command. The fan provides airflow. We do not claim that it removes humidity or lowers the room temperature.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 3
Objectives
03 / 12
Build a readable nine-rule Mamdani controller.
Visualize membership functions and explain a worked example.
Check coverage, bounds and invalid inputs across the declared domain.
Evolve expression trees to approximate simulated outputs.
Notes: Our objectives are to define fuzzy sets, build nine understandable rules, implement the controller, and test its response. A separate genetic programming experiment learns an approximation of simulated fuzzy outputs. We report model limitations instead of claiming measured energy savings.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 4
System Design
04 / 12
Variable | Domain | Meaning
Temperature | 15–40 °C | Room condition input
Humidity | 20–90% RH | Room condition input
Fan command | 0–100% | Requested speed, not RPM
Validate → Fuzzify → Min rules → Max aggregation → Centroid
Software simulation. A future motor driver needs calibration.
Notes: Temperature ranges from fifteen to forty degrees Celsius. Relative humidity ranges from twenty to ninety percent. The output is a normalized fan command from zero to one hundred percent. We validate, fuzzify, evaluate rules, aggregate consequents, and calculate the centroid. Hardware integration remains future work.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 5
Membership Functions
05 / 12
Chart: 
| 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0
Low | 1 | 0.91667 | 0.83333 | 0.75 | 0.66667 | 0.58333 | 0.5 | 0.41667 | 0.33333 | 0.25 | 0.16667 | 0.083333 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Medium | 0 | 0 | 0 | 0 | 0 | 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 0.875 | 0.75 | 0.625 | 0.5 | 0.375 | 0.25 | 0.125 | 0 | 0 | 0 | 0 | 0
High | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.090909 | 0.18182 | 0.27273 | 0.36364 | 0.45454 | 0.54546 | 0.63636 | 0.72727 | 0.81818 | 0.90909 | 1
Temperature (°C)
Humidity: (20,20,55)
(35,60,85), (65,90,90)
Output: (0,0,50)
(25,50,75), (50,100,100)
Temperature sets: (15,15,27), (20,28,36), (29,40,40)
Notes: Each variable has low, medium and high triangular memberships. Shoulder sets cover the ends of the domain. A reading can belong partly to more than one set. These degrees are memberships, not probabilities. The thresholds are illustrative classroom design choices.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 6
Nine Fuzzy Rules
06 / 12
Temperature / Humidity | Low | Medium | High
Low | Low | Low | Medium
Medium | Low | Medium | High
High | High | High | High
Example: IF temperature is Medium AND humidity is High, THEN fan command is High.
Notes: The table contains nine rules. Each row is a temperature set and each column is a humidity set. For example, medium temperature and high humidity request high fan speed. High temperature requests high speed at every humidity level. Every rule has equal weight.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 7
Implementation
07 / 12
AND: αᵢⱼ = min(μtemperatureᵢ, μhumidityⱼ)
Aggregate: A(z) = max over rules of min(αᵢⱼ, μoutput(z))
Command: ∫ z A(z) dz / ∫ A(z) dz
NumPy integration with a 0.1-point output grid. Invalid inputs raise ValueError.
Notes: The main implementation uses NumPy, so scikit fuzzy is not required. AND takes the minimum membership. Each output set is clipped at its rule strength. Maximum combines all clipped sets. Trapezoidal integration calculates the output centroid on a zero point one percentage point grid. Invalid inputs raise an error.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 8
Worked Example: 30 °C, 80% RH
08 / 12
Input | Low | Medium | High
30 °C | 0.000 | 0.750 | 0.091
80% RH | 0.000 | 0.200 | 0.600
Medium output clips at 0.200. High output clips at 0.600.
73.113% fan command
Notes: At thirty degrees, medium temperature membership is zero point seven five. At eighty percent humidity, high membership is zero point six. The strongest rule clips the high output at zero point six. Medium output also activates at zero point two. Their aggregated centroid gives a seventy three point one one three percent fan command.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 9
Simulation Results
09 / 12
Temperature (°C) | Humidity (%RH) | Command (%)
15 | 20 | 16.667
22 | 40 | 29.848
28 | 60 | 50
30 | 80 | 73.113
35 | 50 | 67.328
40 | 90 | 83.333
Low/high shoulder centroids limit this design to about 16.67–83.33%.
Notes: The examples span cool, moderate and warm conditions. Twenty eight degrees and sixty percent humidity gives fifty percent. Forty degrees and ninety percent gives about eighty three point three three percent. A shoulder output reaches its centroid inside its support, so the command does not reach one hundred percent.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 10
Analysis and Verification
10 / 12
Chart: 
| 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0
30% RH | 17.7248 | 17.7248 | 17.7248 | 17.7248 | 18.0555 | 18.7091 | 19.4444 | 20.2485 | 20.673 | 19.4444 | 18.3712 | 17.7248 | 17.7248 | 17.7248 | 17.7248 | 27.0061 | 34.7135 | 42.123 | 49.5926 | 57.8269 | 67.8549 | 81.7172 | 82.2752 | 82.2752 | 82.2752 | 82.2752
60% RH | 16.6666 | 16.7735 | 17.0634 | 17.4999 | 18.0555 | 18.7091 | 25.5622 | 31.4241 | 36.2415 | 40.2146 | 43.6746 | 46.8667 | 50 | 50 | 50 | 53.3987 | 56.8132 | 60.4466 | 64.5176 | 69.3282 | 75.0759 | 81.7172 | 82.3594 | 82.8672 | 83.2071 | 83.3334
85% RH | 50 | 50 | 50 | 50 | 50 | 50 | 55.5218 | 60.7242 | 65.5834 | 70.139 | 74.5236 | 78.8207 | 82.7778 | 82.7778 | 82.7778 | 82.5001 | 81.6288 | 80.5556 | 79.327 | 80.1248 | 80.966 | 81.7172 | 82.3594 | 82.7778 | 82.7778 | 82.7778
Temperature (°C)
1,479 valid grid outputs
Local decreases:
1.358 points / 0.5 °C
2.387 points / 2.5% RH
No measured energy or comfort data
Notes: All one thousand four hundred and seventy nine validation points returned finite bounded outputs. The response is continuous, but it has small local decreases. On our test grid the largest temperature step decrease is one point three six percentage points. The largest humidity step decrease is two point three nine points. The report explains these centroid effects.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 11
Genetic Programming
11 / 12
Expression trees with +, −, ×, min and max. Inputs normalize to 0–1.
100 trees, 40 generations, seed 71. Tournament selection and subtree variation.
85 training points + 36 held-out test points from an 11 × 11 grid.
Training RMSE: 9.215 points. Test RMSE: 9.431 points.
Approximation of synthetic fuzzy labels. The main controller remains the nine-rule model.
Notes: Genetic programming evolves expression trees using addition, subtraction, multiplication, minimum and maximum. We use one hundred trees for forty generations with a fixed seed. Eighty five samples train the model and thirty six are held out. Test error is nine point four three one percentage points against the simulated fuzzy target. This experiment does not optimize real comfort.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.

## Slide 12
Conclusion and Next Steps
12 / 12
The controller covers the declared domain and explains its commands.
Local nonmonotonic behavior and GP approximation error remain visible.
Next: calibrate rules, enforce monotonicity and validate a physical fan.
Method references: official scikit-fuzzy control example and DEAP GP tutorial.
Full URLs and experiment details appear in the report and speaker notes.
Notes: The project demonstrates an explainable fuzzy controller and an actual genetic programming approximation. Our deliverables include reproducible code, graphs, a report, and this presentation. Future work includes monotonic response tuning and hardware calibration. Public repository, LinkedIn and video links will be added after the group uploads the files. Thank you.
References: https://scikit-fuzzy.github.io/scikit-fuzzy/auto_examples/plot_tipping_problem_newapi.html ; https://deap.readthedocs.io/en/stable/tutorials/advanced/gp.html . All parameter choices and results are project-specific simulations.